## Slide 1: LAB3. MOTOR VALIDATION
Student ID: 22200576, 22400448
Name: 이주영, 오유성

## Slide 2: 1. Goal of the Experiment
Obtain Motor Static Property
Motor Static Property vs Linearized Model
Linear Mapping
Linearization Validation
Check Slew Rate Limit
Sine Response - Bode Magnitude plot

## Slide 3: 3. Motor Static Property vs Linearized Model
3-Point Mapping:
Quadratic Linearization through selecting 3 exclusive points.
2) Accuracy & Deviations:
The goal is to accurately trace the 3 points, especially near the deadzone region. Though, minor errors do exist in the remaining region.

## Slide 4: 4. Linear Mapping
Input Range:
2) Deadzone Setting:
3) Linear Slope:
]

## Slide 5: 5. Linearization Validation
Full-Range Verification: Applied both triangle and sine waves to sweep the entire spectrum of input .

## Slide 6: 5. Linearization Validation
Deadzone: Deadzone was observed around the control input range of -0.05 V to +0.05 V.
Minimum Peak Distortion: Distortion occurred in the response curve passed through its minimum peak due to the impact of mechanical backlash during the directional reversal.

## Slide 7: 6. Check Slew Rate Limit
Response Linearity: The transient slope of the output increased linearly in proportion to the pulse input magnitude from 0V up to 1.8V.
Limit Verification: The lack of slope saturation confirms that the system is not affected by slew rate limits within the tested operational range.

## Slide 8: 7. Sine Response - Bode Magnitude plot
Sine Wave Input: Evaluated the frequency response by sequentially applying sine wave inputs from DC to 8Hz.
Bandwidth Identification: Determined the system bandwidth to be 3.4Hz by identifying the point where the gain drops to -3dB.